## Slide 1
Mapping Vulnerabilities of the California Food-Energy-Water System under Paleo-Informed Extreme Hydroclimate Conditions
AUTHORS
Rohini S. Gupta1*, Scott Steinschneider2, Patrick M. Reed1
1Civil and Environmental Engineering, Cornell University
2Biological and Environmental Engineering, Cornell University
*Presenting author: rg727@cornell.edu
Water and Society: Water Resources Management and Policy in a Changing World (AGU 2023)
Lake Oroville, May 2021 (source: Noah Berger / AP photo)

## Slide 2: Prominent Extremes and Economic Impacts
Dec 2022-Jan 2023
AR- Driven Flood Event
$1.5 Billion
Jan-Feb 2017
AR- Driven Flood Event
$1.7 Billion
2007-2009
Feb 11-20, 1986
$1.1 Billion
AR- Driven Flood Event
$1 Billion/Year
1986-1992
Drought
Drought
2020-2022
$1 Billion/Year
2012-2016
Drought
$10 Billion
Drought
>$1 Billion/Year
Introduction | Reservoir Risk | Groundwater Bank Risk | Water Delivery Risk | Conclusion

## Slide 3: A holistic representation of risk to individual stakeholders is dependent on many interconnected factors.
Hydroclimatic
Factors
State of the System
Stakeholder
Attributes
Introduction | Reservoir Risk | Groundwater Bank Risk | Water Delivery Risk | Conclusion

## Slide 4: A holistic representation of risk to individual stakeholders is dependent on many interconnected factors.
State of the System
Stakeholder
Attributes
Extreme Events Experienced
Has the stakeholder experienced all possible magnitudes, frequencies, and sequences of extreme events?
Hydroclimatic
Factors
Introduction | Reservoir Risk | Groundwater Bank Risk | Water Delivery Risk | Conclusion

## Slide 5: A holistic representation of risk to individual stakeholders is dependent on many interconnected factors.
State of the System
Stakeholder
Attributes
v
Extreme Events Experienced
Increased demands, changes to operating rules, prioritization of environmental flows? Are water reserves available or depleted?
Current policy, operating rules
v
v
Groundwater/ Reservoir Storage States
Hydroclimatic
Factors
Introduction | Reservoir Risk | Groundwater Bank Risk | Water Delivery Risk | Conclusion

## Slide 6: A holistic representation of risk to individual stakeholders is dependent on many interconnected factors.
State of the System
Stakeholder
Attributes
v
Extreme Events Experienced
What water contracts does the stakeholder have? What is the priority of their water rights?
Current policy, operating rules
v
v
Groundwater/ Reservoir Storage States
Water Rights
Diversity of Water Sources
Hydroclimatic
Factors
Introduction | Reservoir Risk | Groundwater Bank Risk | Water Delivery Risk | Conclusion

## Slide 7: To comprehensively quantify risk to a complex system, you need:
A detailed model of the system (individual users, water rights, groundwater banking, conveyance)
A large ensemble of highly variable and temporally dynamic hydrology
Introduction | Reservoir Risk | Groundwater Bank Risk | Water Delivery Risk | Conclusion

## Slide 8: To comprehensively quantify risk to a complex system, you need:
A detailed model of the system (individual users, water rights, groundwater banking, conveyance)
A large ensemble of highly variable and temporally dynamic hydrology
Introduction | Reservoir Risk | Groundwater Bank Risk | Water Delivery Risk | Conclusion

## Slide 9: We have a highly resolved simulation model of CALFEWS.
https://github.com/hbz5000/CALFEWS
Daily timescale operation of >1000 critical institutional and infrastructure elements
dams, water conveyance systems, groundwater banks, and water allocation decisions.
Introduction | Reservoir Risk | Groundwater Bank Risk | Water Delivery Risk | Conclusion

## Slide 10: To comprehensively quantify risk to a complex system, you need:
A detailed model of the system (individual users, water rights, groundwater banking, conveyance)
A large ensemble of highly variable and temporally dynamic hydrology
Introduction | Reservoir Risk | Groundwater Bank Risk | Water Delivery Risk | Conclusion

## Slide 11: We have a large ensemble of 600-year daily streamflow traces for CALFEWS.
Tree-ring based reconstruction captures 600-years of natural variability, including megadroughts and pluvials.
Method provides multiple realizations of plausible weather conditioned on regional circulation patterns.
Introduction | Reservoir Risk | Groundwater Bank Risk | Water Delivery Risk | Conclusion

## Slide 12: There is large non-stationarity in flood and drought extremes (even in the absence of anthropogenic climate changes).
A flood event that has a 1% chance of occurring on any given year
Introduction | Reservoir Risk | Groundwater Bank Risk | Water Delivery Risk | Conclusion

## Slide 13: There is large non-stationarity in flood and drought extremes (even in the absence of anthropogenic climate changes).
The modern record underestimates flood (and drought) hazard
Introduction | Reservoir Risk | Groundwater Bank Risk | Water Delivery Risk | Conclusion

## Slide 14: There is large non-stationarity in flood and drought extremes (even in the absence of anthropogenic climate changes).
4x capacity of Don Pedro
Reservoir (10 km3)
Introduction | Reservoir Risk | Groundwater Bank Risk | Water Delivery Risk | Conclusion

## Slide 15: We isolate out a dynamic period from 1520-1640.
Late 1500s megadrought
Early 1600s
Pluvial
Introduction | Reservoir Risk | Groundwater Bank Risk | Water Delivery Risk | Conclusion

## Slide 16: How vulnerable is the CALFEWS system under highly variable and dynamic paleo-informed hydrology from 1520-1640?
Introduction | Reservoir Risk | Groundwater Bank Risk | Water Delivery Risk | Conclusion

## Slide 17: How vulnerable is the CALFEWS system under highly variable and dynamic paleo-informed hydrology from 1520-1640?
We explore this vulnerability at multiple time scales and locations within the system
Reservoirs
Groundwater
Banks
Contract
Deliveries
Introduction | Reservoir Risk | Groundwater Bank Risk | Water Delivery Risk | Conclusion

## Slide 18: Reservoir Risk
Introduction | Reservoir Risk | Groundwater Bank Risk | Water Delivery Risk | Conclusion

## Slide 19
Lake Oroville
Source: Josh Edelson/AFP/Getty Images

## Slide 20
Lake Oroville
Source: Josh Edelson/AFP/Getty Images

## Slide 21: We capture a greater variation in monthly storage than modern drought periods.
Spread of monthly storages across 50, 30-year traces in the driest part of megadrought period
Introduction | Reservoir Risk | Groundwater Bank Risk | Water Delivery Risk | Conclusion

## Slide 22: We capture a greater variation in monthly storage than modern drought periods.
Shading represents how many months we generate that have a storage less than the y -axis value
Introduction | Reservoir Risk | Groundwater Bank Risk | Water Delivery Risk | Conclusion

## Slide 23: We capture a greater variation in monthly storage than modern drought periods.
2007-2009
2012-2016
Worst monthly storage observed under modern droughts are overlaid for comparison
Introduction | Reservoir Risk | Groundwater Bank Risk | Water Delivery Risk | Conclusion

## Slide 24: We capture a greater variation in monthly storage than modern drought periods.
The megadrought traces lead to many instances (~18,000 months) where Oroville reaches dead pool in summer months which are important for irrigation.
Max Capacity= 3537 tAF Deadpool= 825 tAF
2007-2009
2012-2016
Introduction | Reservoir Risk | Groundwater Bank Risk | Water Delivery Risk | Conclusion

## Slide 25: Groundwater Banks
Introduction | Reservoir Risk | Groundwater Bank Risk | Water Delivery Risk | Conclusion

## Slide 26
Kern Water Bank
Source: Kern Fan Project, 2023

## Slide 27
Kern Water Bank
Almost three times the storage capacity of nearby Lake Isabella. (1.5 million acre-feet of water)
Water is stored underground during wet years and recovered during dry years for agricultural and municipal and industrial uses.
Introduction | Reservoir Risk | Groundwater Bank Risk | Water Delivery Risk | Conclusion

## Slide 28
Largest Account Holder
Smaller Account Holder
Kernel density plots of monthly groundwater bank balances
Mega
drought
Pluvial
Mega
drought
Pluvial
Introduction | Reservoir Risk | Groundwater Bank Risk | Water Delivery Risk | Conclusion

## Slide 29
Largest Account Holder
Smaller Account Holder
Mega
drought
Pluvial
Mega
drought
Pluvial
Strong regime shift in mass of distribution from megadrought to pluvial period
Introduction | Reservoir Risk | Groundwater Bank Risk | Water Delivery Risk | Conclusion

## Slide 30
Largest Account Holder
Smaller Account Holder
Mega
drought
Pluvial
Mega
drought
Pluvial
Risk during highly variable periods is not homogenous across users.
Introduction | Reservoir Risk | Groundwater Bank Risk | Water Delivery Risk | Conclusion

## Slide 31
Largest Account Holder
Smaller Account Holder
Mega
drought
Pluvial
Mega
drought
Pluvial
Smaller account holder relies heavily on drawing groundwater during megadrought periods when surface water is reduced.
Introduction | Reservoir Risk | Groundwater Bank Risk | Water Delivery Risk | Conclusion

## Slide 32: Contract Deliveries
Introduction | Reservoir Risk | Groundwater Bank Risk | Water Delivery Risk | Conclusion

## Slide 33: Water Contracts
Entitles owners to some amount of surface water that are associated with one or more reservoirs and withdrawals from canals and rivers.
Reservoir
Water Contract
San Luis (state)
San Luis (federal)
Millerton
Pine Flat
Kaweah
Success
Isabella
State Water Project
Central Valley Project/Exchange Contractors (senior)
Central Valley Project/Delta Division
Central Valley Project/Cross Valley Contractors
Central Valley Project/ Friant Division Class 1 (senior)
Central Valley Project/ Friant Division Class 2
Kings River Water Rights holder
Kaweah River Water Rights holders
Tule River Water Rights holders
Kern River Water Rights holders
Introduction | Reservoir Risk | Groundwater Bank Risk | Water Delivery Risk | Conclusion

## Slide 34: Water Contracts
Entitles owners to some amount of surface water that are associated with one or more reservoirs and withdrawals from canals and rivers.
Reservoir
Water Contract
San Luis (state)
San Luis (federal)
Millerton
Pine Flat
Kaweah
Success
Isabella
State Water Project
Central Valley Project/Exchange Contractors (senior)
Central Valley Project/Delta Division
Central Valley Project/Cross Valley Contractors
Central Valley Project/ Friant Division Class 1 (senior)
Central Valley Project/ Friant Division Class 2
Kings River Water Rights holder
Kaweah River Water Rights holders
Tule River Water Rights holders
Kern River Water Rights holders
Introduction | Reservoir Risk | Groundwater Bank Risk | Water Delivery Risk | Conclusion

## Slide 35: We capture a greater variation in monthly minimum contract deliveries than the worst modern drought.
The frequency at which deliveries of a specific magnitude are experienced during 1550-1580 megadrought period.
Introduction | Reservoir Risk | Groundwater Bank Risk | Water Delivery Risk | Conclusion

## Slide 36: We capture a greater variation in monthly minimum contract deliveries than the worst modern drought.
Black line represents minimum monthly deliveries through 2012-2016 drought
Introduction | Reservoir Risk | Groundwater Bank Risk | Water Delivery Risk | Conclusion

## Slide 37: We capture a greater variation in monthly minimum contract deliveries than the worst modern drought.
Shading represents the frequency at which deliveries of a specific magnitude are experienced in our megadrought traces (dark green= more common)
Introduction | Reservoir Risk | Groundwater Bank Risk | Water Delivery Risk | Conclusion

## Slide 38: We capture a greater variation in monthly minimum contract deliveries than the worst modern drought.
We create many yearly traces that are characterized by lower deliveries than the worst deliveries seen in the modern day drought
Introduction | Reservoir Risk | Groundwater Bank Risk | Water Delivery Risk | Conclusion

## Slide 39: Conclusion
1
A holistic representation of risk is important for stakeholders to be able to make well-informed decisions about risk-reducing investments.
Introduction | Reservoir Risk | Groundwater Bank Risk | Water Delivery Risk | Conclusion

## Slide 40: Conclusion
1
A holistic representation of risk is important for stakeholders to be able to make well-informed decisions about risk-reducing investments.
2
We use a highly resolved simulation model + large paleo-driven hydrology ensemble to explore the bounds of risk at multiple tiers of the CALFEWS system.
Introduction | Reservoir Risk | Groundwater Bank Risk | Water Delivery Risk | Conclusion

## Slide 41: Conclusion
1
A holistic representation of risk is important for stakeholders to be able to make well-informed decisions about risk-reducing investments.
2
We use a highly resolved simulation model + large paleo-driven hydrology ensemble to explore the bounds of risk at multiple tiers of the CALFEWS system.
3
We demonstrate that paleo-driven variability can create lower reservoir levels and water deliveries than those experienced in the worst modern droughts. Inequalities across users of groundwater banks and surface water contracts reflects system complexities.
Introduction | Reservoir Risk | Groundwater Bank Risk | Water Delivery Risk | Conclusion

## Slide 42
Thank you! Questions?
This work is supported by the National Science Foundation Graduate Research Fellowship Program under Grant No. DGE-1650441. The views expressed in this presentation are those of the authors and do not necessarily reflect the views or policies of the National Science Foundation.
Water and Society: Water Resources Management and Policy in a Changing World (AGU 2023)
Lake Oroville, May 2021 (source: Noah Berger / AP photo)

## Slide 43
Slide 2 References
Water and Society: Water Resources Management and Policy in a Changing World (AGU 2023)
Lake Oroville, May 2021 (source: Noah Berger / AP photo)
Moore, Nancy Young, Ellen M. Pint, and Lloyd Dixon, Assessment of the Economic Impacts of California's Drought on Urban Areas: A Research Agenda. Santa Monica, CA: RAND Corporation, 1993. https://www.rand.org/pubs/monograph_reports/MR251.html.
Anderson, Lorena (2022) Last Year’s Drought Cost Ag Industry More than 1 Billion, Thousands of Jobs, New Analysis Shows (https://news.ucmerced.edu/news/2022/last-year%E2%80%99s-drought-cost-ag-industry-more-1-billion-thousands-jobs-new-analysis-shows)
Castleman, Terry (2023). California storm costs could add up to nation’s first billion-dollar disaster of 2023 (https://www.latimes.com/california/story/2023-01-10/california-storm-costs-could-add-up-to-nations-first-billion-dollar-disaster-of-2023)
Drought Cost California 1 Billion in 1991 (https://www.nytimes.com/1992/01/25/us/drought-cost-california-1-billion-in-1991.html)