## Slide 1
Stress Testing California's Water System using an Exploratory Ensemble Analysis Conditioned on the Late Renaissance Megadrought and Climate Change
H51I - Water and Society: Water Resources Management and Policy in a Changing World (AGU 2024)
Lake Oroville, May 2021 (source: Noah Berger / AP photo)
AUTHORS
Rohini S. Gupta1*, Scott Steinschneider1, Harrison B. Zeff2 , Patrick M. Reed3
1Biological and Environmental Engineering, Cornell University
2 University of North Carolina at Chapel Hill
3Civil and Environmental Engineering, Cornell University
*Presenting author: rg727@cornell.edu

## Slide 2
California experiences extreme hydroclimate volatility that poses challenges for the region’s water system planning and management.
2021
2023
Source: Justin Sullivan/Getty Images
Source: CA DWR
Lake Oroville
Introduction | Methods | Results | Conclusions

## Slide 3
California’s cycles of flood and drought are intensifying under climate change.
Introduction | Methods | Results | Conclusions

## Slide 4
California’s cycles of flood and drought are intensifying under climate change, but impacts are hard to predict.
1
Extremes result from co-evolution of climate change with natural variability.
Introduction | Methods | Results | Conclusions

## Slide 5
California’s cycles of flood and drought are intensifying under climate change, but impacts are hard to predict.
Extremes result from co-evolution of climate change with natural variability.
1
California has experienced megadroughts and megaflood events in absence of human activity.
The Great Flood of 1862
Source: San Bernadino Sun
Introduction | Methods | Results | Conclusions

## Slide 6
California’s cycles of flood and drought are intensifying under climate change, but impacts are hard to predict.
Extremes result from co-evolution of climate change with natural variability.
1
Extremes can be amplified due to external forcings like human-driven warming.
Introduction | Methods | Results | Conclusions

## Slide 7
California’s cycles of flood and drought are intensifying under climate change, but impacts are hard to predict.
2
v
Hydroclimate Extremes
Vulnerabilities to users are shaped by how extremes will propagate through California’s complex water system.
Introduction | Methods | Results | Conclusions

## Slide 8
California’s cycles of flood and drought are intensifying under climate change, but impacts are hard to predict.
2
v
Hydroclimate Extremes
Current policy, operating rules
v
Groundwater/ Reservoir Storage States
v
Vulnerabilities to users are shaped by how extremes will propagate through California’s complex water system.
Introduction | Methods | Results | Conclusions

## Slide 9
California’s cycles of flood and drought are intensifying under climate change, but impacts are hard to predict.
2
v
Hydroclimate Extremes
Current policy, operating rules
v
Groundwater/ Reservoir Storage States
v
Water Rights
Diversity of Water Sources
Vulnerabilities to users are shaped by how extremes will propagate through California’s complex water system.
Introduction | Methods | Results | Conclusions

## Slide 10
Motivating Question
How can we comprehensively map the impacts of hydroclimate extremes through the state’s institutionally complex water system and down to its diverse users?
Introduction | Methods | Results | Conclusions

## Slide 11
Motivating Question
How can we comprehensively map the impacts of hydroclimate extremes through the state’s institutionally complex water system and down to its diverse users?
Comprehensively understanding a user’s risk requires exploring the range of vulnerabilities that manifest under many different scenarios.
Introduction | Methods | Results | Conclusions

## Slide 12
Motivating Question
How can we comprehensively map the impacts of hydroclimate extremes through the state’s institutionally complex water system and down to its diverse users?
Comprehensively understanding a user’s risk requires exploring the range of vulnerabilities that manifest under many different scenarios.
We create an exploratory modeling framework that combines
A highly resolved model of California’s water system
A large ensemble of consequential hydrology.
Introduction | Methods | Results | Conclusions

## Slide 13: We have a highly resolved simulation model of the CALFEWS system.
https://github.com/hbz5000/CALFEWS
Daily timescale operation of >1000 critical institutional and infrastructure elements
(dams, water conveyance systems, groundwater banks, irrigation districts)
Introduction | Methods | Results | Conclusions

## Slide 14: We have a large ensemble of 600-year streamflow traces.
Introduction | Methods | Results | Conclusions
Gupta et al., 2023
*Created from a paleo-conditioned weather generator combined with a hydrologic model

## Slide 15: We isolate out a 30-year section of the Late Renaissance Megadrought (1550-1580 CE).
Late Renaissance Megadrought
Introduction | Methods | Results | Conclusions
Gupta et al., 2023

## Slide 16: We layer plausible climate changes on top of megadrought-conditioned weather.
We isolate a scenario of 4 degree temperature increase, and 7% scaling of precipitation.
Introduction | Methods | Results | Conclusions

## Slide 17: Key Questions
How do drought dynamics uncovered in the Late Renaissance Megadrought propagate through California’s modern water system?
1
Introduction | Methods | Results | Conclusions

## Slide 18: Key Questions
How do drought dynamics uncovered in the Late Renaissance Megadrought propagate through California’s modern water system?
How does risk evolve when megadrought dynamics are embedded with plausible climate change signals?
1
2
Introduction | Methods | Results | Conclusions

## Slide 19
Introduction | Methods | Results | Conclusions

## Slide 20
Sacramento and San Joaquin River Basins
Tulare River Basin
Water Conveyance
North
South
Introduction | Methods | Results | Conclusions

## Slide 21
State Water Project
Central Valley Project
Oroville
Shasta
Capacity: 3.5 million acre-feet
Capacity: 4.5 million acre-feet
Largest Reservoir
2nd Largest Reservoir
Introduction | Methods | Results | Conclusions

## Slide 22
State Water Project
Central Valley Project
Oroville
Shasta
Capacity: 3.5 million acre-feet
Capacity: 4.5 million acre-feet
What happens to these reservoirs under megadrought and climate change conditions?
Introduction | Methods | Results | Conclusions

## Slide 23
Shasta
Oroville
Distribution of monthly average storages at each reservoir under megadrought conditions, across all 50 ensemble members.
Introduction | Methods | Results | Conclusions

## Slide 24
Shasta
Oroville
Distribution of monthly average storages at each reservoir under megadrought conditions, across all 50 ensemble members.
Dead pool
Max capacity
Introduction | Methods | Results | Conclusions

## Slide 25
Shasta
Oroville
Megadrought distribution spans dead pool to maximum capacity, with peaks at 60% and 90% capacity.
Introduction | Methods | Results | Conclusions

## Slide 26
Shasta
Oroville
Shift in distributions towards lower storages and dead pool
Introduction | Methods | Results | Conclusions

## Slide 27
Shasta
Oroville
Oroville is 12.5% more likely to reach dead pool than Shasta under the climate change scenario.
Introduction | Methods | Results | Conclusions

## Slide 28
State Water Project
Central Valley Project
Oroville
Shasta
San Luis Reservoir
Deliveries to Districts and Groundwater Banks
Introduction | Methods | Results | Conclusions
Sacramento-San Joaquin Delta

## Slide 29
SWP Delta
Entitle owners to some amount of surface water that are associated with one or more reservoirs and withdrawals from canals and rivers.
State Water Project
Central Valley Project
CVP Delta (Junior)
Source: CA DWR
CVP Exchange
(Senior)
Water Contracts
Introduction | Methods | Results | Conclusions

## Slide 30
Minimum accumulated annual deliveries across all ensemble members and for 5, 10, 15, and 20-year durations
Introduction | Methods | Results | Conclusions

## Slide 31
Introduction | Methods | Results | Conclusions

## Slide 32
Over shorter time periods, users experience similar deliveries under modern and megadrought scenarios.
Introduction | Methods | Results | Conclusions

## Slide 33
Under longer durations, megadrought conditions leads to accumulated deliveries that are 16-36% lower than historical.
Introduction | Methods | Results | Conclusions

## Slide 34
10-year historical deliveries for SWP and CVP Delta would take 20 years to achieve under climate change conditions.
Introduction | Methods | Results | Conclusions

## Slide 35
Kern Groundwater Bank
Capacity: 1.5 million acre-feet of water
Water is stored underground during wet years and recovered during dry years for agricultural, municipal, and industrial uses.
Source: Kern Fan Groundwater Project
Introduction | Methods | Results | Conclusions

## Slide 36
Senior Account
Junior Account
Introduction | Methods | Results | Conclusions

## Slide 37
Senior Account
Junior Account
Under modern conditions, senior account holder bank balance is robust.
Introduction | Methods | Results | Conclusions

## Slide 38
Senior Account
Junior Account
Experiences higher frequency of depleted storages (16% under megadrought vs. 2% under historical conditions)
Experiences instances of depleted storages (0% under historical conditions)
Introduction | Methods | Results | Conclusions

## Slide 39
Senior Account
Junior Account
The probability of groundwater bank balance reaching zero increases by 50% for the junior user and 120% for the senior user.
Introduction | Methods | Results | Conclusions

## Slide 40: Key Findings
1
The Late Renaissance Megadrought is characterized by extended dry conditions that lead to increased frequency of critically low reservoir levels, multi-year periods of below normal deliveries (including to senior rights holders), and depleted groundwater resources.
Introduction | Methods | Results | Conclusions

## Slide 41: Key Findings
1
The Late Renaissance Megadrought is characterized by extended dry conditions that lead to increased frequency of critically low reservoir levels, multi-year periods of below normal deliveries (including to senior rights holders), and depleted groundwater resources.
2
Vulnerabilities become more severe and frequent under plausible climate changes.
Introduction | Methods | Results | Conclusions

## Slide 42: Key Findings
1
The Late Renaissance Megadrought is characterized by extended dry conditions that lead to increased frequency of critically low reservoir levels, multi-year periods of below normal deliveries (including to senior rights holders), and depleted groundwater resources.
2
Vulnerabilities become more severe under plausible climate changes.
3
The risk faced by stakeholders is highly dependent on their water rights, sources of water, and access to groundwater banking.
Introduction | Methods | Results | Conclusions

## Slide 43
Thank you! Questions?
This research was sponsored by the US Department of Energy’s Office of Science as a part of the research in MultiSector Dynamics within the Earth and Environmental System Modeling program. The funding is part of the Integrated Multisector, Multiscale Modeling (IM3) Scientific Focus Area associated with Grant Number DE-AC0576RL01830.
Lake Oroville, May 2021 (source: Noah Berger / AP photo)
H51I - Water and Society: Water Resources Management and Policy in a Changing World (AGU 2024)
Preprint: Rohini S Gupta, Scott Steinschneider, Patrick M. Reed. Exploring Vulnerabilities in the California Water System under the Late Renaissance Megadrought and Climate Change. ESS Open Archive . October 15, 2024.

## Slide 44
Introduction | Methods | Results | Conclusions
Average inflows decline faster at Oroville than Shasta
Difference is due to regression-based representations of seasonally varying upstream activities used to convert FNF to capture current management impacts on reservoir inflows