## Slide 1
Process-Rich Scenario Generation Enhances Exploratory Decision Support for Deeply Uncertain Hydroclimatic Extremes
AUTHORS
Rohini S. Gupta1*, Scott Steinschneider2, Patrick M. Reed1
1Civil and Environmental Engineering, Cornell University
2Biological and Environmental Engineering, Cornell University
*Presenting author: rg727@cornell.edu
2022 DMDU Annual Meeting

## Slide 2: Key Motivation
1
Managing water systems in the Western US is extremely difficult due to extreme interannual volatility that characterizes the region’s hydroclimate.
Introduction | Methods | Exploratory Uses| Case Study | Conclusion

## Slide 3: California experiences extreme hydroclimate volatility.
U.S. Drought Monitor
Introduction | Methods | Exploratory Uses| Case Study | Conclusion

## Slide 4: California experiences extreme hydroclimate volatility.
U.S. Drought Monitor
California has experienced multiple drought cycles in the last two decades.
Introduction | Methods | Exploratory Uses| Case Study | Conclusion

## Slide 5: California experiences extreme hydroclimate volatility.
U.S. Drought Monitor
Each drought cycle has ended with an extreme atmospheric river driven event.
Introduction | Methods | Exploratory Uses| Case Study | Conclusion

## Slide 6
Oroville Dam Failure, 2017

## Slide 7
Lake Oroville, 2021

## Slide 8: Key Motivation
1
2
This volatility is in part driven by natural variability and extremes are being amplified by climate changes.
Introduction | Methods | Exploratory Uses| Case Study | Conclusion
Managing water systems in the Western US is extremely difficult due to extreme interannual volatility that characterizes the region’s hydroclimate.

## Slide 9: Natural variability can produce extreme events.
Tree-ring reconstructions have revealed multiple persistent megadroughts over the past millennium.
The Great Flood of 1862- Turned the Sacramento and San Joaquin valleys into inland seas
Downtown Sacramento following the Great Flood of 1862. The city remained underwater for months, triggering a massive reconstruction project to raise the downtown area 10 to 15 feet. (San Bernadino Sun)
Introduction | Methods | Exploratory Uses| Case Study | Conclusion

## Slide 10: Climate changes can exacerbate extremes.
Introduction | Methods | Exploratory Uses| Case Study | Conclusion

## Slide 11: Key Motivation
1
2
This volatility is in part driven by natural variability and is being amplified by climate changes.
3
Robust planning and management of water systems in the region requires careful generation of states of the world that can capture both drivers effectively.
Introduction | Methods | Exploratory Uses| Case Study | Conclusion
Managing water systems in the Western US is extremely difficult due to extreme interannual volatility that characterizes the region’s hydroclimate.

## Slide 12: A common approach to generating physically plausible future SOWs is by using GCMs
Global
Local
Top-Down
Global Climate Models
Downscale to
Regional
Impact and Adaptation Options
Introduction | Methods | Exploratory Uses| Case Study | Conclusion

## Slide 13: Gap: GCMs do not represent regional dynamics well.
Introduction | Methods | Exploratory Uses| Case Study | Conclusion

## Slide 14: Stochastic tools paired with bottom-up approaches are more robust for conducting regional assessments.
Global
Local
Top-Down
Bottom-Up
Global Climate Models
Downscale to
Regional
Synthetic
generators conditioned on regional weather or streamflow
Impact and Adaptation Options
Introduction | Methods | Exploratory Uses| Case Study | Conclusion

## Slide 15: Stochastic tools paired with bottom-up approaches are more robust for conducting regional assessments.
Global
Local
Top-Down
Bottom-Up
Global Climate Models
Downscale to
Regional
Synthetic
generators conditioned on regional weather or streamflow
Impact and Adaptation Options
Models need to be:
Physically plausible
Extrapolate outside of historical record
Support inclusion of climate changes
Introduction | Methods | Exploratory Uses| Case Study | Conclusion

## Slide 16: Stochastic tools paired with bottom-up approaches are more robust for conducting regional assessments.
Global
Local
Top-Down
Bottom-Up
Global Climate Models
Downscale to
Regional
Synthetic
generators conditioned on regional weather or streamflow
Gap: Availability of stochastic models with these characteristics are limited.
Impact and Adaptation Options
Introduction | Methods | Exploratory Uses| Case Study | Conclusion

## Slide 17: Important drivers will dictate how to manage for future extremes
Time Scale
Climate Change
Driver
Action
Identify prominent climate change signals
Adjust design event estimates
Invest in long term inf
Natural Variability
Dynamic (and reversible) operations and adaptations to stabilize during swings
Prioritize: better seasonal forecasts, hedging contracts
We propose a stochastic weather generator to develop plausible hydroclimate scenarios to inform DMDU that emphasize process and mechanistic understanding of extremes and best represent natural variability.
Introduction | Methods | Exploratory Uses| Case Study | Conclusion

## Slide 18: We need a tool that will facilitate the assessments of interest.
Stochastic weather generators need to:
Create physically plausible weather for the region
Support the ability to create climate change scenarios
Capture the range of natural variability in the weather system
Introduction | Methods | Exploratory Uses| Case Study | Conclusion

## Slide 19: We need a tool that will facilitate the assessments of interest.
Stochastic weather generators need to:
Create physically plausible weather for the region
Support the ability to create climate change scenarios
Capture the range of natural variability in the weather system
Introduction | Methods | Exploratory Uses| Case Study | Conclusion

## Slide 20: A weather regime based-stochastic weather generator allows the generation of physically plausible synthetic weather.
Introduction | Methods | Exploratory Uses| Case Study | Conclusion

## Slide 21: Weather regimes are large-scale persistent pressure patterns that influence regional weather.
Gupta, R.S., Steinschneider, S. & Reed, P.M. A multi-objective paleo-informed reconstruction of western US weather regimes over the past 600 years. Clim Dyn (2022). https://doi.org/10.1007/s00382-022-06302-4
Introduction | Methods | Exploratory Uses| Case Study | Conclusion
Pressure Pattern Anomalies
Precipitation Anomalies

## Slide 22: Weather regimes are large-scale persistent pressure patterns that influence regional weather.
Gupta, R.S., Steinschneider, S. & Reed, P.M. A multi-objective paleo-informed reconstruction of western US weather regimes over the past 600 years. Clim Dyn (2022). https://doi.org/10.1007/s00382-022-06302-4
Introduction | Methods | Exploratory Uses| Case Study | Conclusion
Above average precipitation linked to atmospheric rivers

## Slide 23: Weather regimes are large-scale persistent pressure patterns that influence regional weather.
Gupta, R.S., Steinschneider, S. & Reed, P.M. A multi-objective paleo-informed reconstruction of western US weather regimes over the past 600 years. Clim Dyn (2022). https://doi.org/10.1007/s00382-022-06302-4
Introduction | Methods | Exploratory Uses| Case Study | Conclusion
Drought Conditions

## Slide 24: Weather regimes are large-scale persistent pressure patterns that influence regional weather.
Gupta, R.S., Steinschneider, S. & Reed, P.M. A multi-objective paleo-informed reconstruction of western US weather regimes over the past 600 years. Clim Dyn (2022). https://doi.org/10.1007/s00382-022-06302-4
Introduction | Methods | Exploratory Uses| Case Study | Conclusion
Spatially heterogeneous (dipole) conditions

## Slide 25: A weather regime based-stochastic weather generator allows the generation of physically plausible synthetic ensembles.
Identify and simulate WRs which dictate daily large-scale atmospheric flow
Introduction | Methods | Exploratory Uses| Case Study | Conclusion

## Slide 26: A weather regime based-stochastic weather generator allows the generation of physically plausible synthetic ensembles.
Simulate local weather conditioned on weather regimes by bootstrapping from historical record
Introduction | Methods | Exploratory Uses| Case Study | Conclusion

## Slide 27: A weather regime based-stochastic weather generator allows the generation of physically plausible synthetic ensembles.
Hierarchical connection between WRs and local weather helps maintain complex space-time relationship
Introduction | Methods | Exploratory Uses| Case Study | Conclusion

## Slide 28: We need a tool that will facilitate the assessments of interest.
Stochastic weather generators need to:
Create physically plausible weather for the region
Support the ability to create climate change scenarios
Capture the range of natural variability in the weather system
Introduction | Methods | Exploratory Uses| Case Study | Conclusion

## Slide 29: A weather regime based-stochastic weather generator allows the generation of physically plausible synthetic ensembles.
Apply thermodynamic climate changes to the generated ensembles
Introduction | Methods | Exploratory Uses| Case Study | Conclusion

## Slide 30: Thermodynamic climate changes can be applied post-generation.
Temperature Trends
Precipitation Scaling
Scale upper and lower quantiles of precipitation distribution consistent with applied warming (0-14% per degree C)
Apply stepwise warming to each grid cell (0-4°C)
Introduction | Methods | Exploratory Uses| Case Study | Conclusion

## Slide 31: Thermodynamic climate changes can be applied post-generation.
Temperature Trends
Precipitation Scaling
Can constrain ranges based on GCM projections or localized studies
Apply stepwise warming to each grid cell (0-4°C)
Introduction | Methods | Exploratory Uses| Case Study | Conclusion
Scale upper and lower quantiles of precipitation distribution consistent with applied warming (0-14% per degree C)

## Slide 32: We need a tool that will facilitate the assessments of interest.
Stochastic weather generators need to:
Create physically plausible weather for the region
Support the ability to create climate change scenarios
Capture the range of natural variability in the weather system
Introduction | Methods | Exploratory Uses| Case Study | Conclusion

## Slide 33: The weather generator can accommodate boundary forcing that dictates weather regime evolution.
The key to enhanced natural variability representation in generated weather lies in using appropriate boundary forcing.
Introduction | Methods | Exploratory Uses| Case Study | Conclusion

## Slide 34: We reconstruct weather regime occurrence back to the year 1400 CE.
Introduction | Methods | Exploratory Uses| Case Study | Conclusion

## Slide 35: We demonstrate the variability in weather regime dynamics prior to the instrumental period.
The extent of WR variability in the reconstruction extends well past what is observed during the instrumental period.
Gupta, R.S., Steinschneider, S. & Reed, P.M. A multi-objective paleo-informed reconstruction of western US weather regimes over the past 600 years. Clim Dyn (2022). https://doi.org/10.1007/s00382-022-06302-4
Introduction | Methods | Exploratory Uses| Case Study | Conclusion

## Slide 36: We demonstrate the variability in weather regime dynamics prior to the instrumental period.
By conditioning our generator on the instrumental period, we are severely under-representing natural variability.
Gupta, R.S., Steinschneider, S. & Reed, P.M. A multi-objective paleo-informed reconstruction of western US weather regimes over the past 600 years. Clim Dyn (2022). https://doi.org/10.1007/s00382-022-06302-4
Introduction | Methods | Exploratory Uses| Case Study | Conclusion

## Slide 37: We use the reconstructed WR dynamics to drive the weather generator.
This allows us to generate 600 years of daily precipitation and temperature through the extent of the reconstruction.
Introduction | Methods | Exploratory Uses| Case Study | Conclusion

## Slide 38: We then pair the generated weather with hydrologic models to get ensembles of streamflow for the region.
Introduction | Methods | Exploratory Uses| Case Study | Conclusion

## Slide 39: We generate flood and drought metrics from the hydrology ensembles.
Flood
Peak flows corresponding to 10-Yr and 100-Yr design events
Drought
SSI-Index based metrics for occurrence, severity, and duration
Introduction | Methods | Exploratory Uses| Case Study | Conclusion

## Slide 40: Example Exploratory Uses
Introduction | Methods | Exploratory Uses | Case Study | Conclusion

## Slide 41: This tool creates SOWs that:
1. Preserve spatial correlation across multiple sites and basins
Mechanism: Conditioning on synoptic scale WRs
Result: Allows for the creation of internally consistent multi-basin weather ensembles (currently conditioned on 15 watersheds in the Central Valley region)
Introduction | Methods | Exploratory Uses | Case Study | Conclusion

## Slide 42: This tool creates SOWs that:
2. Allow better assessment of compound risk to basins
Mechanism: Internally consistent weather generation
Result: Provides more robust way to characterize spatially compounding flood or drought risk which poses more serious water system management challenges
Introduction | Methods | Exploratory Uses | Case Study | Conclusion

## Slide 43: This tool creates SOWs that:
3. Capture a wide range of natural variability
Mechanism: Incorporation of reconstructed WR dynamics
Result:
Paleo-reconstruction includes key megadrought (late 1500s) and paleo-flood periods (early 1600s)
Better representation of drought-flood pathways
Introduction | Methods | Exploratory Uses | Case Study | Conclusion

## Slide 44: This tool creates SOWs that:
4. Map how thermodynamic changes lead to changes in metrics of interest
Mechanism: Systematic layering of temperature trends or precipitation scaling
Result: Clearly delineate the effects of specific climate changes on metrics of interest
Introduction | Methods | Exploratory Uses | Case Study | Conclusion

## Slide 45: Example Case Study
Introduction | Methods | Exploratory Uses | Case Study | Conclusion

## Slide 46: Ensembles from this study will be used to force California food-energy-water system model.
Abstracts critical institutional and infrastructure elements (>1,000) that capture the complex dynamics of water balance for north-central California.
We provide inflow to the 12 main reservoirs
Introduction | Methods | Exploratory Uses | Case Study | Conclusion

## Slide 47: Conclusion
1
Assessing the robustness of water resources systems in California to extremes requires careful generation of states of the world that capture plausible future hydroclimate.
Introduction | Methods | Exploratory Uses | Case Study | Conclusion

## Slide 48: Conclusion
1
2
A weather-regime based stochastic weather generator allows the generation of physical plausible and internally-consistent (and climate change-informed) weather and streamflow for this region.
Introduction | Methods | Exploratory Uses | Case Study | Conclusion
Assessing the robustness of water resources systems in California to extremes requires careful generation of states of the world that capture plausible future hydroclimate.

## Slide 49: Conclusion
1
2
3
Introduction | Methods | Exploratory Uses | Case Study | Conclusion
Internally consistent weather generation provides a mechanism to explore challenging compound risk across basins and to characterize vulnerabilities to regional water systems.
Assessing the robustness of water resources systems in California to extremes requires careful generation of states of the world that capture plausible future hydroclimate.
A weather-regime based stochastic weather generator allows the generation of physical plausible and internally-consistent (and climate change-informed) weather and streamflow for this region.

## Slide 50
Thank you! Questions?
AUTHORS
Rohini S. Gupta1*, Scott Steinschneider2, Patrick M. Reed1
1Civil and Environmental Engineering, Cornell University
2Biological and Environmental Engineering, Cornell University
*Presenting author: rg727@cornell.edu
DMDU Annual Meeting 2022

## Slide 51: Mid-Latitudes
Introduction | Methods | Exploratory Uses | Case Study | Conclusion
Include subtropical and temperate zones